1. (15 points) The random process X(n) is created by a spinning dial that lands on the number 0 with probability 1/4, and on the number 2 with probability 3/4. So a typical run looks like

0 2 2 2 2 2 0 2 0 0 2 2 2 2 0 2 2 2 2 2  …. (15 2's, 5 0's)

If my example misled you to use probabilities 1/3 and 2/3, I will give full credit.

What are the mean 1.5 ; autocorrelation R(n) = 2.25 if n ( 0,  3 if n = 0 ; and auto covariance C(n) = 0 if n ( 0,  .75 if n = 0 ; for this process? Don't forget the zero-time-lag case. Is the process stationary? Yes   Ergodic? Yes

2. (10 points) The random variable Y is defined as the sum of X(1) and X(2) (in Problem 1). Plot the probability density function fY(y) for Y. Use delta functions to express the formula for fY(y).

3. (25 points) Suppose that X(t) is a zero-mean stationary Gaussian process with autocorrelation function   .

(a) What is the standard deviation of X(1)?  1

(b) What is the joint probability density fX(0),X(2)(x1,x2) of X(0) and X(2)?

(c) If X(0) is determined to be 0, what are the (conditional) mean 0 and standard deviation ((1-e-8)  of X(2)?

(d) What is the conditional probability density for X(0), given that X(2) = 0 ?

(e)  Are  X(0) and X(2) independent? No

4. (15 points) What is the power spectral density of y(n) if   y(n+1) = 0.5 ( y(n) + 3 ( v(n) , where v(n) is zero-mean white Gaussian noise with power 10 ?

5. (15 points) What is the autocorrelation function for y(n) if

y(n+1) = 0.5 ( y(n) + 3 ( v(n) , where v(n) is zero-mean white Gaussian noise with power 10 ?

Method One. To put this system into the form of the Yule Walker equations rewrite as   x(n) = 0.5 x(n-1) + 3 v(n-1), and since v(n-1) is white noise, and thus stationary, call it w(n).              x(n) = 0.5 x(n-1) + 3 w(n) = -a(1) x(n-1) + b(0) w(n) .

So a(1) = -0.5,  b(0) = 3,  all other coefficients are zero, (v2 = 10 .

With rn as the autocorrelation RX(n), the Y-W equations are

r0(1 + r1(a(1) = b(0)2 (V2 ,           or             r0 - .5r1 = 90

r1(1 + r0(a(1) = 0                          or             -.5r0 + r1 = 0

….

rm(1 + rm-1(a(1) = 0                       or              rm = .5rm-1 .

Solution is

r0 = 120

r1 =   60

r2 =  30

r3 =  15

…

Method Two.  The autocorrelation function is the inverse Fourier transform of the power spectral density, which was found in Problem 4.

6. (20 points) Try to fit a process x(n) whose autocorrelation function RX(m) equals  with a (1,0) ARMA model. (State the difference equation for the model and find the coefficients.) Since I made a typo, I won't take off any points for this. I will give partial credit for exceptional attempts at repair.

The Yule-Walker equations are the same as in Problem 5, but now we know r0 = 1 and r1 = .5 .

r0(1 + r1(a(1) = b(0)2 (V2 ,   or  1 + .5 a(1) = 10b(0)2 ,  or    .5 a(1) - 10b(0)2 = -1 .

r1(1 + r0(a(1) = 0                                                            or    .5 + a(1) = 0 .

Solution is   a(1) = -.5,   b(0) = (.075